## Slide 1
Smart Agriculture Monitoring
IoT Final Project - Virtual Sensors, MQTT, Gateway Processing, and Real-Time Alerts
A complete virtual IoT pipeline designed to satisfy the final-project requirements.
Sensors -> Publisher -> MQTT Broker -> Gateway -> Subscriber
Group X | Editable deck | Replace placeholders before final submission
Temperature
Humidity
MQTT
Alerts
CAI26442 | Smart Agriculture Monitoring | Slide 1

## Slide 2
Project Requirements Covered
Mapping the assignment checklist to the implemented solution
Sensors
Temperature + Humidity virtual sensor simulation
JSON Data
device_id, two readings, status, timestamps
MQTT
Public broker + unique raw/processed topics
Gateway
Validation, enrichment, and alert logic
Subscriber
Real-time terminal monitoring output
Deliverables
Report PDF/DOCX, code, screenshots, PPTX
CAI26442 | Smart Agriculture Monitoring | Slide 2

## Slide 3
System Architecture
Required pipeline implemented exactly as specified
CAI26442 | Smart Agriculture Monitoring | Slide 3

## Slide 4
Data Model and MQTT Topics
What is sent, where it flows, and why it is valid
{ "device_id": "groupX_agri_node_01", "temperature": 33.2, "humidity": 63, "status": "RAW" }
Publisher payload: valid JSON
Raw Topic
iot/project/groupX/agriculture/raw
Processed Topic
iot/project/groupX/agriculture/processed
Gateway Output
Timestamp + status + alert_reason + gateway_id
CAI26442 | Smart Agriculture Monitoring | Slide 4

## Slide 5
Gateway Processing and Decision Logic
Validation first, alert classification second
Validation
Required fields + numeric types + humidity range
Enrichment
UTC timestamp + gateway identifier
Publish
Processed JSON to subscriber topic
Alert Rules
Rule 1
temperature >= 32 C
ALERT
Rule 2
humidity >= 80%
ALERT
Rule 3
temperature >= 29 C OR humidity <= 35%
WARNING
Default
No threshold triggered
NORMAL
CAI26442 | Smart Agriculture Monitoring | Slide 5

## Slide 6
Runtime Evidence: Publisher and Gateway
Screenshots included in the package and replaceable with live-run captures
Publisher: JSON every 2-3 sec
Gateway: validation + status
CAI26442 | Smart Agriculture Monitoring | Slide 6

## Slide 7
Runtime Evidence: Subscriber and Alert
Real-time monitoring output and threshold trigger
Subscriber monitoring
Alert condition example
CAI26442 | Smart Agriculture Monitoring | Slide 7

## Slide 8
Conclusion and Demonstration Flow
A 5-10 minute presentation structure
• The project meets the required virtual IoT architecture.
• Two sensors, JSON modeling, MQTT publish/subscribe, gateway processing, and alerts are implemented.
• The live demo can be shown in three terminal windows: gateway, subscriber, publisher.
• Replace GroupX and member placeholders before submission.
1. Gateway
Start processing layer
2. Subscriber
Start monitoring output
3. Publisher
Generate readings
Ready for demonstration
CAI26442 | Smart Agriculture Monitoring | Slide 8